## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
Smart Dryer
Matteo Baschieri
Valentina Grieci

## Slide 2: Introduction
Washing and drying clothes is a necessary everyday activity.
There are already several devices designed to solve the problem of drying clothes.
Our study aims to create a low-cost smart system to optimize this process.
Drying Rack
Dryer
Electric drying rack

## Slide 3: Poll and Market Analysis
 | Not much | Quite enough | A lot
How much is important that the clothes dry fast? | 16,5% | 47,1% | 36,5%
How much is important that a drying system has little dimensions? | 11,8% | 60% | 29,4%
How much is important that drying system is quiet? | 3,5% | 35,3 | 61,2%
Considering a drying system would you choose: | (1) | (2)
Fast but expensive Slow but cheap | 23,5 % | 76,5%
Fast but with high consumption Slow but with low consumption | 9% | 89,4%
Comparison of the main characteristics of the drying systems

## Slide 4: System Description
The moisture content can be approximated as a linear function of time:
Total time to dry the clothes:
Where
T [min]
q [-]
With:

## Slide 5: System Specification and General Architecture
The system must:
make the drying process faster,
understand when the clothes are dry,
notice the user that the clothes are dry.
Sensor I
Microcontroller
Drying component
Battery
Packaging
User interface
Sensor II
Schematic representation of the system

## Slide 6: System Characteristics
Possible positioning of the module on different drying rack
=module
Customer preferences adaptable
three modalities:
fast drying: fan always on until the drying is complete;
normal regime: 5 minutes on and 5 off, repeat until the drying is complete;
energy saving: 3 minutes on and 9 off, repeat until the drying is complete.
Customer rack adaptable

## Slide 7: Prototype
Humidity sensor DHT11
Sunon MEC0381V1-A99 fan
Prototype photo
Evaluate drying
Drying
component
Fan
Humidity sensor

## Slide 8: Experiments: physical model
OPERATING REGIME | Fan always off q=0 | 2 min off 1 min on q=0,33 | 1 min off 1 min on q=0,5 | 2 min off 2 min on q=0,5 | 3 min off 3 min on q=0,5 | 2 min off 1 min on q=0,66 | Fan always on q=1
TIME | 113 min | 48 min | 33 min | 38 min | 32 min | 30 min | 21 min
Comparison between experimental and theoretical results

## Slide 9: Experiment: real application
Humidity and temperature over time in the final test of the system

## Slide 10: Conclusion
Advantages:
Good time efficiency
Cheap
Low consumption
Small size
Quiet
Further improvment:
Explicit to find the optimum and so the optimal fan.
Insert a motor to tilt the fan in order to cover a bigger portion of the rack.

## Slide 11
Thank you for your attention!